## Slide 1
CS 118: Local Area Networks, Ethernet and 802.11
George Varghese
October 26, 2017

## Slide 2: BOB METCALFE – ETHERNET
PhD Thesis at Harvard invents CSMA/CD
Goes to Xerox PARC and helps invent Ethernet
Founds 3 Com to commercialize Ethernet
Internet Hall of Fame

## Slide 3
Data Link Sublayers
ERROR DETECTION
FRAMING
FRAMING
ERROR DETECTION
MEDIA ACCESS
MULTIPLEXING
Point−to−point Links (2 nodes)
(e.g., HDLC, Frame Relay)
Broadcast Links (>= 2 nodes)
(e.g., Ethernet, Token Ring)
ERROR RECOVERY
(OPTIONAL)
Bits
Bits
Frames
Frames
QUASI-RELIABLE 1 HOP FRAME PIPE

## Slide 4
A Rose by any other Name
Inherently sequential. Link shared among multiple senders. A.K.A.
Multiaccess links because there are multiple nodes that may simultaneously access link.
Broadcast links because every transmission can be heard by all other stations.
Local Area Networks or LANs because the geographical area serviced by a LAN is local and small – from 1-10 Kms, covering an office, a building, or at most a campus.

## Slide 5
Cost: Connect up all computers in a building, office, campus. 200-1000 users. Saves wiring costs to share one wire (or the air waves, no dedicated air waves).
Bandwidth: Provides high bandwidth and low error rates for local group of users. Worth it because most high-bandwidth distributed computing (e.g., file servers etc.) has acess locality.
Statistical Multiplexing: Time division multiplexing not a good idea when user traffic is bursty as data is. Bursty = high peak/average ratio. Each user gets access to entire LAN bandwidth when other users are idle. As more users are added, they share the bandwidth
WHY LANS

## Slide 6
Statistical versus Strict Multiplexing
Strict multiplexing: TDM or FDM where a user is given a fixed allocation regardless of whether the user has data to send or not.
Bursty: traffic has a high peak/average ratio.
Analysis: gives each user B/N , where N is the number of possible sources; stat multiplexing attempts to give each user, B/x, where x is the number of busy users. N large (100 -1000) while x is small (1-10).
Example: Suppose 100 users each transfer a 125 kbyte file every 2 hours. At 10 Mbps, a 125 kbyte file takes 0.1 seconds to transmit. At 0.1 Mbps, file takes 10 seconds to transfer.

## Slide 7
ALOHA
UNSLOTTED ALOHA
SLOTTED ALOHA
Ethernet Predecessor: Multiple ground stations in various parts of Hawai.
Problem: Couldn’t detect collisions or sense when channel was busy. Similar problems in 802.11
Slotted Aloha: reduces vulnerable period by half but requires a common clock
2T
T

## Slide 8
In transmission collision detection
and semi-reliability
1500 byte frame involved in a collision. Ethernet aborts transmission after 64 bytes. Aloha will send the entire 1500 bytes and detect when ack is not received. Better for large frames, and large frame sizes allow efficiency.
No detection of frame corruption. (1 in million). However, collisions are frequent. Semi-reliable: detect collisions and retransmit in hardware.

## Slide 9
Dynamic Backoff
Consider 2 colliders. One should wait 1 slot and the other 0. Can approximate by tossing a coin.
Consider 16 colliders. Ordinary coin-tossing does not work. Pick random numbers from 1 to 16.
static scheme either does not work for a large number of colliders or is inefficient for a small number.
Binary exponential backoff.

## Slide 10
ETHERNET
Three main mechanisms: :
Carrier sense and deference: No point transmitting when someone else is speaking
Collision Detection: Stop large frame (< 1500 bytes) when after 64 bytes you detect a collision.
Exponential Backoff: Collisions very frequent, so must retransmit. Random backoff avoids synchronized collisions. Dynamically adjust to number of colliders.

## Slide 11
ETHERNET CONTINUED
Smaller mechanism to make main ideas work:
Slot time: = 2T, T is 1-way propagation delay limited to 51.2 usec = 64 bit times at 10 Mbps: maximum delay to detect a collision.
Minimum packet size: 64 bytes to avoid finishing transmission before collision is detected. Add pad if needed.
Jam: transmit small number of bits after you detect a collision to ensure that other transmitters also detect collision.
Collision detection: One way is to use Manchester with average DC level per bit. Collision detection by detecting increased voltage level.

## Slide 12
Ethernet Header
LLC sublayer
01010111 preamble | Dest (6) | Source (6) | Length (2) | Data | Pad | CRC
Total Frame length 64<=L<=1500

## Slide 13
Why Min Packet Sizes
A
B
COLLISION
Clean
jam to
ensure
"width"
of collision
Short
Frame
•
•

## Slide 14
Ethernet Implementation Details
Limited distance (2.5 km). 500 m wires. 4 repeaters.
Thin wire, Thick wire
Repeaters/Hubs: important device, reads in a bit and writes out a bit on other side, boosting signal strength.
Physical Topology is a star or tree.

## Slide 15
Cost of statistical muxing in Ethernet
If distance goes up by a factor of 10 or speed, then what happens to min packet size? Why is it wasteful?
100 Mbps Ethernet proposal has only 200 m extent.
Gigabit Ethernet? Span too small (2 m? What kind of LAN is that?) Instead, replace shared wire with point to point links and hubs with switches.

## Slide 16
From CSMA to switching
•
•
A
B
S
R
•
•
A
B
S
R
HUB
HUB
SWITCH
SWITCH
If A talks to R at same time as B talks to S there is
a collision. True for 10 and 100 M Ethernet.
A can talk to R at same time as B talks to S with
no collision. Switch buffers and allows parallel
connections. True for Gigabit Ethernet

## Slide 17
So you are telling me that
Gigabit Ethernet no longer uses CSMA/CD
So why do we do study the stuff?
Because similar Media Access protocols are used especially in wireless and 802.11 as we now describe

## Slide 18
Concepts
Statistical Multiplexing
Importance of Pipe-size or bandwidth delay product in determining efficiency.
Logical versus physical topology. 10 M Ethernet is logically a bus but physically a star

## Slide 19
802.11
George Varghese
(slides from A. Snoeren, UCSD)

## Slide 20
802.11 Layering
•
•
access point
fixed
terminal
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure
network
LLC
LLC

## Slide 21: WLAN: IEEE 802.11b
Data rate
  1, 2, 5.5, 11 Mbit/s
  User data rate max. approx. 6 Mbit/s
Transmission range
  300m outdoor, 30m indoor
  Max. data rate ~10m indoor
Frequency
  Free 2.4 GHz ISM-band

## Slide 22: Physical Channels
US (FCC)/Canada (IC)
2400
[MHz]
2412
2483.5
2437
2462
channel 1
channel 6
channel 11
22 MHz
12 channels available for use in the US
  Each channel is 22 MHz wide
  Only 3 orthogonal channels
  Using any others causes interference

## Slide 23: Carrier Sense Multiple Access
CSMA: listen before transmit:
If channel sensed idle: transmit entire pkt
If channel sensed busy, defer transmission
  Persistent CSMA: retry immediately with probability p when channel becomes idle (may cause instability)
  Non-persistent CSMA: retry after random interval

## Slide 24: Hidden Terminal Problem
A
B
C
B can communicate with both A and C
A and C cannot hear each other – not a single shared channel
Problem
  When A transmits to B, C cannot detect the transmission using the carrier sense mechanism
  If C transmits, collision will occur at node B
Solution:
  Hidden sender C needs to defer
Notes: Carrier sense is useful but not all interfering senders can be carrier sensed. This results in a problem, commonly called hidden terminal.

## Slide 25: RTS/CTS (MACA)
A
B
C
When A wants to send a packet to B, A first sends a Request-to-Send (RTS) to B
On receiving RTS, B responds by sending Clear-to-Send (CTS), provided that A is able to receive the packet
When C overhears a CTS, it keeps quiet for the duration of the transfer
  Transfer duration is included in both RTS and CTS

## Slide 26: Backoff Interval
Problem: With many contending nodes, RTS packets will frequently collide
Solution: When transmitting a packet, choose a backoff interval in the range [0, CW]
  CW is contention window
Wait the length of the interval when medium is idle
  Count-down is suspended if medium becomes busy
  Transmit when backoff interval reaches 0
Need to adjust CW as contention varies
  Similar in spirit to Ethernet backoff

## Slide 27: Non-symmetric ranges
C
F
A
B
E
D
DATA
Transmit “range”
Carrier sense
range
F

## Slide 28: 802.11 COLLISION AVOIDANCE EXAMPLE
C
F
A
B
E
D
RTS
RTS = Request-to-Send
Pretending a circular range

## Slide 29: IEEE 802.11
C
F
A
B
E
D
RTS
RTS = Request-to-Send
NAV = 10
NAV = remaining duration to keep quiet

## Slide 30
C
F
A
B
E
D
CTS
CTS = Clear-to-Send

## Slide 31
C
F
A
B
E
D
CTS
CTS = Clear-to-Send
NAV = 8

## Slide 32
C
F
A
B
E
D
DATA
DATA packet follows CTS. Successful data reception acknowledged using ACK.

## Slide 33
C
F
A
B
E
D
ACK
Reserved area