## Slide 1
CS118: Lecture 2, Networking Overview, Take 2
George Varghese
WORLDWIDE
INTERNET

## Slide 2
Lecture Outline
Prize Question on Layering
Hourglass model
Overview of email transfer
Begin Physical Layer

## Slide 3
PRIZE QUESTION 1
How can we detect congestion at network level and send it to TCP at the sender without violating strict layering

## Slide 4
Communications is complicated
  Modulation and encoding bits
  Splitting sequences of bits into packets
  Routing
  Recovering from lost messages etc….
Really hard to think about all of this and get it right
Not all applications need all of it
How to achieve interoperability?
PROBLEM BEING SOLVED

## Slide 5
Sub-divide the problem
  Each layer relies on services from layer below
  Each layer exports services to layer above
Interface between layers defines interaction
  Hides implementation details (encapsulation)
  Layers can change without disturbing other layers (modularity)
Interface among peers in a layer is a protocol
  If peers speak same protocol, they can interoperate
LAYERING IS MODULAR DESIGN

## Slide 6
How do you divide functionality across the layers?
End-to-end argument [Saltzer84]
  Functionality should be implemented at a lower layer iff it can be correctly and completely implemented there. Incomplete versions of a function can be used as a performance enhancement, but not for correctness
Early, and still relevant, example
  ARPAnet provided reliable link transfers
  Was this enough for reliable communication?
  No, packets could still get corrupted on host-switch link, or inside of the switches
  Hence, still need reliability at higher layers (TCP)
KEY DESIGN DECISION IN IP

## Slide 7
Network
Innovation? Science?
Data Link
Physical
Applications
The Hourglass Model
“Thin Waist”
FTP
HTTP
Video
TCP
UDP
IP
Fiber
Wireless
Cable
Transport
Q: Why was TCP/IP successful?
A: IP addressing (Lecture 12)
Socket interface (Lecture 17)
TCP SUCCESSFUL > 40 years
Notes: Is networking merely plumbing? What can possibly be cool about plumbing compared to deep learning and computation ecology? What is left to do after 40 years of Internet design besides mere engineering and tinkering? Where is the innovation? Where is the science

## Slide 8
MAIL FROM ASKEW TO MARIA
mail chuck@maria
Hi!
ASKEW
MARIA
IP
ROUTER
The setting and the characters in the play

## Slide 9
Sending Bits
We can send bits as energy at the sender and we recover bits by sampling at receiver
Q: How do we where to sample?
A: Clock recovery (Lecture 4)

## Slide 10
Framing Bits
We need to group bits into frames to attach headers. Easy on Ethernet
Q: How do we do it only with bits?
A: Bit Stuffing (Lecture 6)
Energy
No Energy
No Energy

## Slide 11
jim
sally
router
Boom!
Jim
Backs off
askew Wins
D2
D1
askew
D2
SYNCHRONIZING SENDERS
(on the old Ethernet)
Q: How do we detect collisions/backoff?
A: Multi-access LANs (Lecture 9)

## Slide 12
IP ROUTER
128.21.8.2
128.21.11.4
128.21.7.8
128.20.16.13
maria
D4
D3
Network 128.20.*
Network 128.21.*
IP AND ETHERNET ADDRESSES
Q: Why two different addresses?
A: UIDs vs Hierarchy (Lecture 12)

## Slide 13
R1
ASKEW
R2 ROUTER
R3
Whois R2?
Who is R3?
R2 is D2
R3 is D4
MARIA
Remember R2 is D2
Remember
D2
D1
D3
D4
D2 R3 TH MH Hi
D4 R3 TH MH Hi
FORWARDING, ADDRESS RESOLUTION
Q: How to avoid a table of all IP addresses
A: Prefix Lookups (Lecture 13)

## Slide 14
TRANSPORT (TCP) CONNECTIONS
MARIA
ASKEW
TCP PROGRAM
TCP PROGRAM
NETWORK
Well−known Extensions
Local Extension
socket
11
Q: Are there other IPC abstractions
A: Yes, say RPC (Lecture 17)

## Slide 15
TRANSPORT (TCP) CONNECTIONS
Mail Extension ?
12
ASKEW
TCP PROGRAM
MARIA
TCP PROGRAM
Local Extension x
Connected ME,x
ME,x,Data,Seq 1
ME,x,Ack,Seq 1
Shut Down ME,x
OK
Q: Why a 3 way handshake to start?
A: Delayed Duplicates (Lecture 18)

## Slide 16
MAIL PROTOCOL IN ACTION
ASKEW MAIL PROGRAM
MARIA MAIL PROGRAM
Let’s boogie
OK
Deliver to "Chuck" OK
Text is "Hi"
OK
Gotta run
OK
13
Q: What happens if one end crashes
A: Need application state (not in course)