## Slide 1
CS118: Lecture 5, Physical Layer
George Varghese
October 2018

## Slide 2: REVIEW: WHERE IS THE PHYSICAL LAYER?
ROUGHLY, what happens when I click on a Web page from UCLA?
www.google.com
?
My computer
Internet

## Slide 3: Web request (HTTP)
Turn click into HTTP request
GET http://www.google.com/ HTTP/1.1
Host: www.google.com
Connection:keep-alive
…

## Slide 4: Name resolution (DNS)
Where is www.google.com?
What’s the address for www.google.com
My computer
(132.239.9.64)
Oh, you can find it at 66.102.7.104
Local DNS server
(132.239.51.18)

## Slide 5: Data transport (TCP)
Break message into packets (TCP segments)
Should be delivered reliably & in-order
GET http://www.google.com HTTP/1.1
Host: www.google.com
Connection:keep-alive
…
GET htt
1
p://www.
2
google.c
3
“and let me know when they got there”

## Slide 6: Network Layer: Global Network Addressing in IP
Address each packet so it can traverse network and arrive at host
My computer
(132.239.9.64)
www.google.com
(66.102.7.104)
GET htt
1
66.102.7.104
132.239.9.64
Destination
Source
Data

## Slide 7: Network Routing in IP
Qwest
Sprint
UUNet
AT&T
UCLA
www.google.com
(66.102.7.14)
Each router forwards packet towards destination

## Slide 8: Data Link scheduling (Ethernet)
Break message into frames
Media Access Control (MAC)
  Can I send now? Can I send now?
Send frame
Receiver

## Slide 9: Physical layer
802.11b Wireless
Access Point
Ethernet switch/router
To campus
backbone
2.4Ghz Radio
DS/FH Radio
(1-11Mbps)
Cat5 Cable (4 wires)
100Base TX Ethernet
100Mbps
62.5/125um 850nm MMF
1000BaseSX Ethernet
1000Mbps

## Slide 10
PHYSICAL LAYER: SUBLAYERS
Input Stream Output Stream 01010000 01010000
3
Sublayer
Coding Sublayer
Sublayer
Input Signal
Output Signal
Media Transmission
Media Reception
Decoding Sublayer
Coded Stream
Coded Stream
Signal Transmission Sublayer
(SHANNON AND NYQUIST LIMITS)

## Slide 11
Why Study Media
Media affects Protocol Design
  Reinforced Concrete to Skyscapers
We need to understand media tradeoffs when architecting networks
  Think of flashlights versus semaphores

## Slide 12
Media Affects Protocols
Low Bandwidth led to tight encoding:
Early Phone lines, not needed on LANs
Broadcast LANs led to use of Multicast:
Initialization and free copies, to IP multicast.
Building wiring led to Switching: Wiring closets to hubs to ATM switches.
Fiber led to rings: Point-to-point fibers lead to rings.
Fiber led to Digital: Long haul telephone network becomes digital.
Wireless leads to low bandwidths again:
Laptops. Need Ipv6 compression on wireless links!

## Slide 13: Wireless
Widely varying channel bandwidths/distances
Extremely vulnerable to noise and interference
Freq (Hz)
104
106
108
1010
1012
1014
AM
Coax
Microwave
Satellite
Fiber
FM
Twisted
Pair
TV
Radio
UV
Microwave
IR
Light

## Slide 14: Spectrum Allocation
Time (min)
Frequency (Hz)
Policy approach forces spectrum to be allocated like a fixed spatial resource (e.g. land, disk space, etc)
Reality is that spectrum is time and power shared
Measurements show that fixed allocations are poorly utilized
Hot topic: Whitespace communication

## Slide 15
UART
CPU
MODEM
MODEM
UART
CPU
Twisted Pair
RS−232
Low bandwidth
Cheap, Easy to Install
TWISTED PAIR COPPER

## Slide 16: TWISTED PAIR INSIDER VIEW
Typical examples
  Category 5/6 Twisted Pair 10M-10Gbps 50-100m
  Coaxial Cable 10-100Mbps 200m
twisted pair
copper core
insulation
braided outer conductor
outer insulation
coaxial
cable
(coax)

## Slide 17
Using Twisted Pair for Higher Rates Today
Standard twisted pair is limited by loading cables by telephone company to 4 Mhz. Shannon limit is around 56 Kbps (not counting compression). Two alternatives:
Better quality twisted pair cables for local area networks e.g., Cat 3 (10 Mbps, Manchester), Cat 5 (100 Mbps, 100 Mhz bandwidth uses 4-5 coding)
Telephone company removes loading cables, reduces your length, and gives you ADSL. Asymmetrical.

## Slide 18
CPU
CPU
TERMINAL
CPU
Coaxial Cable
Adaptor
Transceiver
Transceiver
Adaptor
High bandwidth (10−100 MHz)
Hard to tap, expensive to Install Small Distance (1 − 3 km without repeaters)
BASEBAND CABLE (e.g. ETHERNET)

## Slide 19
Using Coaxial Cable Today
Coaxial cable has high bandwidth. Used for original 10 Mbps Ethernet but very clunky. Twisted pair (e.g. Cat 5) used today.
Cable still used in cable networks for cable TV and for data via cable modems. Divide bandwidth into 6 Mhz channels for each TV channel and one 6 Mhz channel for downstream data. Theoretically can reach 30 Mbps but beware other users and bandwidth limits. Upstream much less.

## Slide 20
Direct Signal
Slow Signal
FIBRE OPTICS
Photodiode
LED
Laser
Huge Bandwidth (10 Million Mhz!)
Almost Imposible to Tap Point−to−point Secure
Excellent Electrical Isolation
Thin and Easy to Install
Optics still expensive Unidirectional

## Slide 21: Fiber Optics: more physical view
Typical examples
  Multimode Fiber 100Mbps-10Gb 500-2000m
  Single Mode Fiber 1-100Gbps 100m-40km
Cheaper to drive
(LED vs laser) &
terminate
Longer distance
(low attenuation)
Higher data rates
(low dispersion)

## Slide 22
CROWDED CITY
TOWER
TOWER
MICROWAVE
Avoids Right of Way
May be cheaper than installing cable Reasonable Bandwidth
Has problems with Rain
Upto 100 km distance

## Slide 23
SATELLITE
DISH
DISH
Avoids Right of Way Good Bandwidth (500 Mhz) World Wide
Large Latency Antenna Cost

## Slide 24
Wireless Data Options
802.11: Wireless LANs using a wireless access point (AP) at hot spot using unlicensed frequency band 2.4 to 4.485 Ghz (radio frequency) 100 metres. 11 Mbps with 802.11b. Needs hotspot but becoming common and very cheap!
Bluetooth: ad hoc personal area networks with no AP. Master-slave. 4 Mbps
WiMax: broader geographical range smaller bandwidth of a few Mbps
3 G (Cellular telephone networks carrying data) at a few Mbps such as EVDO. Unlimited geographical range and true mobility

## Slide 25
802.11b in some more detail
AP configured with a SSID that you can see when doing View Available Networks and a channel number from 1 to 11. Non-overlapping channels (1 6, 11) can be used to triple bandwidth
Each AP periodically sends a beacon containg SSID.
Each AP scans all 11 channels looking for beacons to get a list of networks. Some choice of AP and then mobile sets up an association
Access protocol to send data tricky because of hidden terminal problem. Mobile A can send to base station and so can Mobile B, but A and B cannot hear each other but can interfere at base station. Needs careful protocol design (later)

## Slide 26
Medium | Speed | Distance Span | Pros | Cons
Twisted Pair | 1 Mps -1 G (Cat 1 – Cat 5) | 1 – 2 Km | Cheap, easy to install | Low distance
Digital Coax | 10-100 Mbps | 1- 2 km | broadcast | Hard to install in building
Analog Coax | 100-500 Mbps | 100 Km | Cable companies Use it now | Expensive amplifiers
Fiber | Terabits | 100 km | Security, low noise, BW | No broadcast, Needs digging
Microwave | 10-100 Mbps | 100 km | Bypass, no right Of way need | Fog outages
Satellite | 100-500 Mbps | worldwide | Cost independent of distance | 250 msec delay Antenna size
RF/Infrared | 1 – 100 Mbps, < 4 Mbps | 1 km 3 m | wireless | Obstacles for infrared
MEDIA PROS AND CONS

## Slide 27
Last Mile
Bottleneck
Twisted Pair, cable, radio
Trans-oceanic Bottleneck fiber, satellite
Crowded City Bottleneck,
Microwave, Radio
PUMPING BITS GLOBALLY

## Slide 28
Sublayer
Sublayer
Input Signal
Output Signal
Media Transmission
Media Reception
Coded Bit Stream
Coded Bit Stream
ETHERNET SUBLAYERS
Input Bit Stream Output Bit Stream 01010000 01010000
Decoding
MEDIA (COAXIAL CABLE)
Manchester
Synchronous Coding

## Slide 29
Problems in all layers
Resource Sharing: FDM/TDM
Addressing: TDM time slots
Synchronization: clock recovery, spacing apart levels
Interconnection Physical layer repeaters are called hubs